## Slide 1
2. Radiometric Properties of Light

## Slide 2
Radiometry
  Objective measure—photodetector
  Cases: Unravel the properties of light in an absolute, unbiased sense
Photometry
  Physiological response of the human retina—human eye
  Cases: Consumer cameras, displays
  What kind of quantities of an electromagnetic ﬁeld are most commonly used in radiometry?
2. Radiometric Properties of Light

## Slide 3
Energy Q: Quantifies ability to perform work
  Accelerating particles, heating materials, generating photoelectrons in a detector, etc
Energy is measured in Joules(J)
Energy conversion generate light
  Thermal to optical: An incandescent bulb
  Electrical to optical: Electrically-pumped laser
  Chemical to optical: Fireflies, chemically-excited lasers
  Light-matter interactions
  Inelastic: An optical field exchange energy with various materials
  Elastic: Light change direction of propagation (or momentum), without loss (or gain) in energy
2.1 Energy

## Slide 4
Energy density W: Energy concentration in space
  V—A certain(finite) volume in space
  Q—Energy
  The same 1 J of energy can produce very different outcomes when distributed over 1 m3 vs. 1 m3 (An 18-order of magnitude difference).
2.2 Energy Density
Q
V
Figure 2.1. Energy density is the ratio of energy Q to the volume V, W=Q/V.

## Slide 5
Power P
  Energy exchanged (emitted, absorbed, detected, reflected, transmitted, scattered, etc.) per unit time
  Peak power vs Average power
  In a very short period of time (peak power)
    Nuclear plant P: ~4GW(410-9 W)
    Femtosecond lasers: P=40GW, 1 mJ in a pulse of 25 fs long (1 fs=10-15 s)
  In a second (average power)
    Nuclear plant: 4GJ/s=4GW
    Femtosecond lasers: 1 kJ/s=1kW(1μs a pulse, 106 pulses per second)
2.3 Power
Source
Figure 2.2. Power radiated by a source is the energy delivered per unit time.

## Slide 6
Power spectrum S
  The power per unit of optical frequency, v.
  Note: The optical frequency, v (Hz), differs from the angular frequency,  (rad/s).  = 2πv
  The total power P
2.4. Temporal Power Spectrum
Figure 2.3. Temporal power spectrum. The infinitesimal area indicated is the power contained in the vicinity of 1.

## Slide 7
Parseval’s theorem
  The total power of a signal is the same whether it is integrated over its entire spread in time or frequency.
  Note: The integral spans the negative frequencies as well.
2.4. Temporal Power Spectrum

## Slide 8
  For real signal f, the total power in the negative frequencies is the same as in the positive frequencies.
  The power spectrum with respect to the wavelength
2.4. Temporal Power Spectrum
(Hermitian)

## Slide 9
  s(v) is a non-negative quantity, can be normalized to a probability density.
  s(v) — the probability of having radiation in the frequency interval (v, v+dv)
  Mean frequency:
  The frequency standard deviation (bandwidth):
2.4. Temporal Power Spectrum
Figure 2.4. Optical spectrum with central frequency and standard deviation defined as first and second order moments of the frequency distribution.

## Slide 10
  Intensity (directional quality)
  The power per unit solid angle, Ω.
  Isotropic emitters: Special sources that emit constant intensity in all directions.
Figure 2.5. a) Representation of an infinitesimal area in the 3D space.
2.5. Intensity: Spatial Power Spectrum

## Slide 11
  The infinitesimal solid angle d Ω:
Figure 2.5. b) Infinitesimal solid angle.
2.5. Intensity: Spatial Power Spectrum

## Slide 12
  Intensity → 2D Spatial power spectrum
  The intensity is the spatial analog of the temporal power spectrum, which can be obtained from the 2D Fourier transform.
2.5. Intensity: Spatial Power Spectrum
Figure 2.5. c) Illustration of how solid angle can be expressed in terms of wave vector.
k
dkx
r
dx
c

## Slide 13
  Irradiance
  The power delivered per unit area.
  Example
  Irradiance of the visible light from the Sun at the surface of the earth: ~103W/m2 (average clear day, at sea level )
  The confocal microscope will deliver a factor of (1 mm/1 μm) 2=106 higher irradiance than a wide-field microscope.
2.6. Irradiance
Figure 2.6. Wide-field vs. confocal illumination. At the same total power, the confocal illumination delivers orders of magnitude higher irradiance.

## Slide 14
  Spectral irradiance
  The power per unit area and unit of optical frequency.
  can describe how the 1KW/m2 irradiance from the sun is distributed over the visible spectrum.
  The spectral irradiance can be expressed in terms of angular frequency interval, , or wavelength, .
2.7. Spectral Irradiance

## Slide 15
  Radiance L(directional quantity)
  The power emitted or absorbed by a surface, per unit solid angle, per unit projected area.
  Lambertian source
  A type of source with constant L, i.e., independent on Ω or Acosθ.
  Lambert’s cosine law
  The intensity has a dependence on angle
2.8. Radiance
Figure 2.7. a) The cosine term in Eq is due to the projection of the source normal onto the direction of interest.

## Slide 16
2.8. Radiance
Figure 2.7. b) Irradiance from a Lambertian in a certain direction source.
Figure 2.7. c) Irradiance from a Lambertian source describes a circle tangent at the source.
  Lambertian source (strongly scattering medium)
  Projector screens used in conference rooms, cloud, diffuser

## Slide 17
2.8. Radiance
Figure 2.8. Conservation of radiance.
  Radiance conservation theorem
  The radiance through a lossless optical system is conserved.
  Implications
  The light can only be spread over a larger area if the angular distribution narrows down accordingly (and vice versa)
    Microscopy— magnification factor of sample plane equals minification factor of angular distribution at the image plane
  The radiance is not conserved in a lossy optical system
  Vignetting or etendue
  Proof of

## Slide 18
2.8. Radiance
  Radiance can be expressed as a distribution in both space and spatial frequency
  dx, dy — the infinitesimal spatial intervals normal to the direction of interest
  For conserved radiance, the space-bandwidth product is constant
(uncertainty relation)
(radiance conservation)
  dx, dkx, dy, dky can be considered as the power-weighted spreads in space and spatial frequency along x and y.

## Slide 19
2.9. Spectral Radiance
  Spectral radiance Lv
  Radiance per unit of frequency
  Lv allows us to characterize the emission from a surface element into a certain direction, with temporal frequency content.
  Lv can be defined with respect to angular frequency, Lω, and wavelength, Lλ, by changing the variable and using the respective Jacobian.

## Slide 20
2.10. Exitance
  Exitance M
  The amount of power emitted by a source per unit area
  Exitance is the property of a source, while irradiance is the property of the field.
  Exitance represents the radiance of the source integrated over all solid angles
  Spectral exitance Mv
  The exitance per unit frequency, or power emitted by the source per unit area, per unit frequency
2.11. Spectral Exitance

## Slide 21
3. Photon-based Radiometric Quantities

## Slide 22
Each photon carries an energy hv or hc/λ
Total energy of optical
N— the number of photons (unitless)
Define an entirely equivalent set of radiometric quantities
  Valuable whenever discrete nature of light is relevant.
  Cases: studying photodetection
3.1. Number of Photons

## Slide 23
Photon density n
  The number of photons per unit volume.
Photon flux Pq
  The photon quantity analogous to power.
  q — a photon quantity
  Connection between Pq and P (power) is straight forward.
3.2. Photon Density
3.3. Photon Flux

## Slide 24
Photon temporal power spectrum Sq
  The photon flux per unit temporal frequency.
Sq(v) — the number of photons per second in the infinitesimal interval (v, v+dv)
Energy-based power spectrum S(v)
3.4. Photon Temporal Power Spectrum

## Slide 25
Photon intensity
  The photon flux per unit solid angle, Ω.
— the spatial power spectrum of the photon flux
3.5. Photon Intensity

## Slide 26
Photon irradiance Iq
  The photon flux per unit area.
Energy-based irradiance
3.6. Photon Irradiance
3.7. Photon Spectral Irradiance
Photon spectral irradiance
  The photon flux per unit area, per unit of optical frequency.

## Slide 27
Photon radiance Lq
  The photon flux emitted or absorbed by a surface, per unit solid angle, per unit projected area.
dAcosθ — the projection of the area normal to the direction of interest
3.8. Photon Radiance
3.9. Photon Spectral Radiance
Photon spectral radiance
  The photon radiance per unit frequency.

## Slide 28
Photon exitance Mq
  The amount of photon flux emitted by a source per unit area.
Note: Photon exitance describes a source, while the photon irradiance is a property of the field and shares the same units.
3.10. Photon Exitance
3.11. Photon Spectral Exitance
Photon spectral exitance
  The photon exitance per unit frequency.

## Slide 29
4. Photometric Properties of Light

## Slide 30
Photometry
  Properties of the light perceived by the human eye (subjective photodetector).
  Spectral sensitivity of the eye is taken into account.
Luminosity function
  The eye spectral response
    Day-time (photopic) adaptation
    Dark time (scotopic) adaptation
  Day time spectral response — Luminous
4. Photometric properties of light
Figure 4.1. Photopic (daytime-adapted, green curve) and scotopic (darkness-adapted blue curve) luminosity functions.

## Slide 31
Luminous energy Ql
  The total energy weighted according to the luminosity function.
  Measured in lumen·second. Lumen is the unit for luminous flux.
4.1. Luminous Energy
Luminous flux (or luminous power) Pl
  The photometric equivalent of power.
  Weighted by the luminosity.
4.2. Luminous Flux

## Slide 32
Luminous energy density Wl
  The luminous energy per unit volume
4.3. Luminous Energy Density
Luminous intensity
  The luminous flux per unit solid angle
  Note: Candela (cd) is a primary units comprising the International System of Units (SI).
4.4. Luminous Intensity

## Slide 33
Standard of candela
  The candela is the luminous intensity in a given direction, of a source that emits monochromatic radiation of frequency 540 × 1012 Hz and that has a radiant intensity in that direction of 1/683 W/rad.
    For the frequency of 540 × 1012 Hz, λ=c/v=555nm, at which the human eye is the most sensitive in bright conditions.
The luminous intensity with respect to wavelength
IΩ — radiometric intensity (in W/srad)
Y(λ) — the photopic luminosity function
evaluated at the particular wavelength
4.4. Luminous Intensity
Figure 4.1. Photopic (daytime-adapted, green curve) and scotopic (darkness-adapted blue curve) luminosity functions.

## Slide 34
Illuminance Il (Equivalent to the photometric irradiance)
  The luminous flux per unit area.
Luminance Ll (Equivalent to the photometric radiance)
  The luminous power per solid angle, per normal unit area of the source.
Brightness is sometimes used interchangeably with luminance.
4.5. Illuminance
4.6. Luminance